## Slide 1
MS4 IDDE Training
For City Field Staff
Tuesday, January 30th 2018

## Slide 3: MS4 Permit
The Municipal Separate Storm Sewer System (MS4) Permit requires permittees to maintain an operations and maintenance program to prevent or reduce pollutant discharges from municipally owned or operated properties. This includes:
  Employee training addressing the importance of protecting water quality and describing MS4 requirements
Why are we doing this?
  Required by state and federal permitting
  Protect our natural resources
  Big Lake is a Level 2 MS4
Outline of Training
  Recognize > Report > Respond

## Slide 4: Illicit Discharge Detection and Elimination (IDDE)
What is the pure IDDE definition?
“…any discharge into the stormwater system that is not composed entirely of stormwater…”
I like to apply common sense, so think of it in terms of a “Discharge beyond an established grass yard or established prairie grass.”
Recognize  Report  Respond!

## Slide 5: Inspection of Stormwater Controls
BMPs
  Silt fence, inlet protection, temporary construction entrance/exit, proper wash out area, hydromulch, biologs, trash coverage
BMPs can be damaged
  Rainstorms
  Construction activities
At a minimum, inspections should include:
  All areas where stormwater typically flows
  All discharge points
  All areas where stabilization has been implemented
  Check to see if controls are implemented and functional
  Check for conditions in which controls may be necessary
City inspection
  Big Lake Permit Requirements
  City Code

## Slide 6: What is a BMP?
Best Management Practices
  A practice, or combination of practices, that is determined to be effective and practicable by being broadly used
  A means of preventing or reducing the amount of pollution generated to a level compatible with water quality goals.
  Silt fence, bio logs, straw blankets, bales, rock entrance, inlet baskets, etc.
Do you see a BMP failing?

## Slide 7: Sources of Stormwater Pollution
Pollutants
  Excess nutrients (nitrogen and phosphorus)
  Hydrocarbons (petroleum compounds)
  Heavy metals
  Pathogens
  Toxic chemicals
  Debris, trash, and litter
Intentional or accident or neglect? Hmmm…

## Slide 8: Look Out For…
Unusual colors and odors
Cloudy or murky appearance
Suds, trash, or debris
Unnatural or excessive vegetation
Leaks, spills, or dumping
Barrels, buckets, 55 gallon drums

## Slide 9: Where should I look?
Construction sites
Dumpsters behind buildings
New home building
Curb lines
Alleyways and parking lots
Loading docks and outdoor storage areas
Near our lakes and rivers
Driveways
City Owned Facilities too!

## Slide 10: MPCA MS4 Training for Parks Maintenance & Stormwater Protection

## Slide 11: On the Lookout for Illegal Discharges Part 1 – detection

## Slide 12: On the Lookout for Illegal Discharges Part 2 – document and report

## Slide 13: MS4 Stormwater Pollution Prevention

## Slide 14: How to Spot an Illicit Discharge

## Slide 15: The Good, The Bad or the Ugly? YOU MAKE THE CALL!

## Slide 39: How Will Our Actions Affect Big Lake?
Property Owners
Lakes
Wetlands
The Elk River
Someday the Mississippi River

## Slide 40: You Can Help Prevent IDDE
Recognize  Report
Big Lake’s legacy of beautiful lakes, wetlands, and rivers

## Slide 41: What to Do
If you see something that looks wrong…
  Report it to your supervisor or Mike Goebel
    Do not confront the person causing the illicit discharge
  If you can’t reach Mike or your supervisor, contact Layne Otteson
  Last resort: if it is a spill with immediate health and safety concerns, call the State Duty office to report and discuss options
    Number: 1-800-422-0798
  Recognize and Report!!!

## Slide 43: Questions or Comments?
Layne Otteson, City Engineer
  763-251-2984
  lotteson@biglakemn.org